## Slide 1: PRISMS Center Center for PRedictive Integrated Structural Materials Science
Brian Puchala, John C. Thomas, Anton Van der Ven
Anirudh Natarajan, John Goiri, Min-Hua Chen, Max Radin, Jonathon Bechtel, Elizabeth Decolvenaere, Anna Belak,
Naga Sri Harsha Gunda, Sanjeev Kolli
TMS ICME 2017
Thurs. May 24, 2017
Website: prisms-center.org
CASM Tutorial – Section 1

## Slide 2: PRISMS Center Integrated Framework
Real Space DFT
(PRISMS-RSDFT)
Fourier Space DFT
(VASP)
Atomic scale
constitutive laws
Statistical Mechanics
(CASM)
Phase Diagrams
(CASM/CALPHAD)
Dislocation Dynamics
(LLNL-ParaDIS)
Phase Field Crystal
(PRISMS-PFC*)
Phase Field
(PRISMS-PF)
Crystal Plasticity
(PRISMS-Plasticity)
Continuum Plasticity
(PRISMS-Plasticity)
Experiments (slip,
twinning, crack, etc.)
Mechano-Chemistry
(PRISMS-MC*)
Experiments

## Slide 3
Phenomenological
descriptions
Electronic structure
Statistical Mechanics
Thermodynamics
Kinetics
Solid Mechanics
Linking atomistic descriptions to phenomenological models of materials
Notes: Many of the most important or useful descriptions of materials behaviour are continuum descriptions.
Phase stability, mechanical properties, and microstructure evolution, can all be understood in terms of the free energy and kinetic coefficients of particular materials.
But of course these quantities fundamentally depend on atomistic interactions.
Our work is focused on using methods of statistical mechanics to link accurate ab initio electronic structure calculations of atomistic systems to phenomenological descriptions of materials.

## Slide 4
Phenomenological
descriptions
Electronic structure
Via rigorous and arbitrarily extendible cluster expansion Hamiltonians
Statistical Mechanics
Cluster Expansion Hamiltonians
Q1
Notes: We do this by constructing cluster expansion effective Hamiltonians in terms of atomic degrees of freedom.
These descriptions are nearly as accurate as electronic structure calculations, but orders of magnitude faster, enabling monte carlo calculations of thermodynamic and kinetic quantities.
The methods we use have many applications, but today I'll just talk about how we've applied it to basic science of the thermodynamics in the Zr-O-H system.

## Slide 5: CASM Tutorial Outline
1:30 – 3:00:
Crystal structure identification & specification
Symmetry analysis
Using CASM to manage data
  Configuration selections and query syntax
  Maintaining sanity with cluster expansion profiles
Cluster expansion basics
  Configuration enumeration
  Cluster expansion basis sets & correlation evaluation
3:30 – 5:00:
Parameterizing cluster expansions
Predicting thermodynamic properties with grand canonical Monte Carlo
Free energy integration and phase diagram construction

## Slide 6: CASM: Clusters Approach to Statistical Mechanics
First-principles energies of a “few” excitations
Lattice Model Hamiltonian
Monte Carlo
Thermodynamics
Extrapolate to
all other excitations

## Slide 7: Tutorial Project: Zr-O binary system
Zr:
  Very high O solubility
ZrOx
  Series of suboxide phases
ZrO2-x
  Oxide
J.P. Abriata, J. Garcés, and R. Versaci, Bulletin of Alloy Phase Diagrams Vol. 7 No. 2 1986 .

## Slide 8: Nature of ZrO1/2 disordering transitions?
“the rearrangement of the oxygen atoms from uneven to even distribution on the neighboring interstice planes, and then [to a] random distribution in each plane.” or is low temperature transition first order?
Arai and Hirabayashi, J. Less-Common Metals, 44, 291 (1976).
Burton, Van de Walle, and Stokes, J. Phys. Soc. Japan, 81, 014004 (2012).

## Slide 9: Problem Definition

## Slide 10: Problem Definition

## Slide 11: Problem Definition
a
b
Lattice Vectors
x
y

## Slide 12: Problem Definition
Basis Atoms
a
b
Lattice Vectors
x
y

## Slide 13: Problem Definition
Lattice Vectors
Basis Atoms
a
b
{
"title" : "ZrO”,
"coordinate_mode" : "Fractional",
"description" : “HCP Zr with oct (O) ",
"lattice_vectors" : [
[ 3.233986860000, 0.000000000000, 0.000000000000 ],
[ -1.616993430000, 2.800714770000, 0.000000000000 ],
[ -0.000000000000, 0.000000000000, 5.168678340000 ]
],
"basis" : [
{
"coordinate" : [ 0.0000000, 0.0000000, 0.000000 ],
"occupant_dof" : [ "Zr" ]
},
{
"coordinate" : [ 0.6666667, 0.3333334, 0.500000 ],
"occupant_dof" : [ "Zr" ]
},
{
"coordinate" : [ 0.3333333, 0.6666667, 0.250000 ],
"occupant_dof" : [ "Va", "O" ]
},
{
"coordinate" : [ 0.3333333, 0.6666667, 0.750000 ],
"occupant_dof" : [ "Va", "O" ]
}
]
}
prim.json:
x
y

## Slide 14: Problem Definition
Lattice Vectors
Basis Atoms
a
b
{
"title" : "ZrO”,
"coordinate_mode" : "Fractional",
"description" : “HCP Zr with oct (O) ",
"lattice_vectors" : [
[ 3.233986860000, 0.000000000000, 0.000000000000 ],
[ -1.616993430000, 2.800714770000, 0.000000000000 ],
[ -0.000000000000, 0.000000000000, 5.168678340000 ]
],
"basis" : [
{
"coordinate" : [ 0.0000000, 0.0000000, 0.000000 ],
"occupant_dof" : [ "Zr" ]
},
{
"coordinate" : [ 0.6666667, 0.3333334, 0.500000 ],
"occupant_dof" : [ "Zr" ]
},
{
"coordinate" : [ 0.3333333, 0.6666667, 0.250000 ],
"occupant_dof" : [ "Va", "O" ]
},
{
"coordinate" : [ 0.3333333, 0.6666667, 0.750000 ],
"occupant_dof" : [ "Va", "O" ]
}
]
}
prim.json:
a
b
c
x
y
x
y
z

## Slide 15: Problem Definition
Lattice Vectors
Basis Atoms
a
b
{
"title" : "ZrO”,
"coordinate_mode" : "Fractional",
"description" : “HCP Zr with oct (O) ",
"lattice_vectors" : [
[ 3.233986860000, 0.000000000000, 0.000000000000 ],
[ -1.616993430000, 2.800714770000, 0.000000000000 ],
[ -0.000000000000, 0.000000000000, 5.168678340000 ]
],
"basis" : [
{
"coordinate" : [ 0.0000000, 0.0000000, 0.000000 ],
"occupant_dof" : [ "Zr" ]
},
{
"coordinate" : [ 0.6666667, 0.3333334, 0.500000 ],
"occupant_dof" : [ "Zr" ]
},
{
"coordinate" : [ 0.3333333, 0.6666667, 0.250000 ],
"occupant_dof" : [ "Va", "O" ]
},
{
"coordinate" : [ 0.3333333, 0.6666667, 0.750000 ],
"occupant_dof" : [ "Va", "O" ]
}
]
}
prim.json:
a
b
c
x
y
x
y
z

## Slide 16: Problem Definition
Lattice Vectors
Basis Atoms
a
b
{
"title" : "ZrO”,
"coordinate_mode" : "Fractional",
"description" : “HCP Zr with oct (O) ",
"lattice_vectors" : [
[ 3.233986860000, 0.000000000000, 0.000000000000 ],
[ -1.616993430000, 2.800714770000, 0.000000000000 ],
[ -0.000000000000, 0.000000000000, 5.168678340000 ]
],
"basis" : [
{
"coordinate" : [ 0.0000000, 0.0000000, 0.000000 ],
"occupant_dof" : [ "Zr" ]
},
{
"coordinate" : [ 0.6666667, 0.3333334, 0.500000 ],
"occupant_dof" : [ "Zr" ]
},
{
"coordinate" : [ 0.3333333, 0.6666667, 0.250000 ],
"occupant_dof" : [ "Va", "O" ]
},
{
"coordinate" : [ 0.3333333, 0.6666667, 0.750000 ],
"occupant_dof" : [ "Va", "O" ]
}
]
}
prim.json:
a
b
c
JSON: JavaScript Object Notation
x
y
x
y
z

## Slide 17: CASM: Getting started
Material
definition
Initialization
Generated
directories

## Slide 18: CASM: Getting started
Install 'casm' command line programs
'casm status'
  Quick look at your current project
  '-n' option: suggestions for next steps
'casm format'
  Documentation of project directory and file formats
'casm –h'
  Help menus show allowed options

## Slide 19: Crystal Symmetry
Apply rotation, reflection, inversion, and/or rotation to the crystal.

## Slide 20: Crystal Symmetry
Apply rotation, reflection, inversion, and/or rotation to the crystal.
60°

## Slide 21: Crystal Symmetry
Apply rotation, reflection, inversion, and/or rotation to the crystal.
If the result is indistinguishable from the initial state, then that operation is in the crystal’s space group.
60°

## Slide 22: Crystal Symmetry
Common notation: {Rα|τ}
  Rα: point group operations such as rotations, reflections, improper rotations, inversions
  τ: translation vector
  α: 3x3 transformation matrix
M.S. Dresselhaus, G. Dresselhaus, and A. Jorio.
Group Theory: Application to the Physics of Condensed Matter.

## Slide 23: Symmetry
Lattice point group:
  Symmetry operations that map lattice onto itself, leaving origin invariant (rotation, mirror, inversion, rotoinversion)
Crystal factor group:
  Symmetry operations that map lattice and identical basis sites onto themselves (translations may result in screw axes or glide planes)
Crystal point group:
  Crystal factor group operations, with translations removed

## Slide 24: Crystal Configurations

## Slide 25: Crystal Configurations

## Slide 26: Crystal Configurations
Vol 2 Supercell
Vol 4 Supercell

## Slide 27: Crystal Configurations

## Slide 28: Crystal Configurations
60°
Equivalent!!

## Slide 29: Supercell Enumeration
Represent lattice using column vector matrices:
P: primitive lattice
S: supercell lattice
T: integer supercell transformation matrix
S1
S2
P1
P2
S1
S2
S1=P1 S2=2P2
S1=P1+P2 S2=-P1+P2

## Slide 30: Supercell Enumeration
Equivalent supercells:
Linear combination of supercell lattice vectors
S
S'

## Slide 31: Supercell Enumeration
Equivalent supercells:
Linear combination of symmetrically equivalent supercell lattice vectors
For a crystal, allowed symmetry operations depends on crystal basis
S
S'

## Slide 32: Supercell enumeration
If unit cell lattice, P, is represented as column vector matrix, then supercell lattices, S, are:
T is an integer supercell transformation matrix, and S has integer volume det(T), relative to the primitive cell.
Supercells are equivalent if for some T:
At a given volume (det(T)), loop over possible T matrices and use crystal point group operations to check if we've found a new symmetrically distinct supercell

## Slide 33: Supercell enumeration
SCEL4_1_4_1_0_0_0
Volume
Shape Factors
Max an min supercell volume can be specified for enumeration
Supercell enumeration can be restricted to 1D and 2D. See casm enum --help
for details.

## Slide 34: Configuration enumeration
A:
B:
Equivalent configurations:
Supercells of the volume 1 configuration

## Slide 35: Configuration enumeration
Equivalent configurations:
Translation maps one configuration onto the other
A:
B:

## Slide 36: Configuration enumeration
Equivalent configurations:
Rotation or translation maps occupants
A:
B:

## Slide 37: Configuration enumeration
Enumerate symmetrically unique configurations by:
  Loop over possible occupations
  Check all factor group operations that keep the supercell lattice vectors unchanged, in combination with all primitive cell translations within the supercell
  If translation within the supercell alone maps all occupants, then it is a supercell of a smaller primitive configuration

## Slide 38: Configuration enumeration
Configurations are enumerated ONLY in supercells that have been enumerated.
You can specify the min and max supercell volumes, or specify a supercell explicitly.
CAUTION: The number of unique configurations that fit in a supercell grows exponentially with supercell volume.

## Slide 39: Configuration visualization
Set up environment:
casm settings --set-view-command 'casm.view VESTA’
Try with one or more configuration names:
casm view SCEL4_2_2_1_0_0_1/25

## Slide 40: CASM Composition metrics
Each configuration has a composition, and there are various ways to measure it:
atom_frac: atom_frac(Au), atom_frac(Cu), etc.
  Number of Au, Cu, etc., divided by total number of atoms. Vacancies are ignored.
comp_n: comp_n(Au), comp_n(Cu), etc.
  Number of Au, Cu, etc., divided by number of primitive cells (volume). Accounts for vacancies.
comp: comp(a), comp(b), etc.
  Primitive-cell-based formula parameters (e.g., AuaCubPt(1-a-b)), determined by user-specified composition axes. Accounts for vacancies.
When vacancies are present, ‘atom_frac’ is qualitatively different from ‘comp_n’ and ‘comp’

## Slide 41: Specifying composition axes
Binary Compound:

## Slide 42: Specifying composition axes
Au
Pt
Cu
Cu1-a-bAubPta
CubAuaPt1-a-b
a
b
a
b
Ternary Compound:
Binary Compound:

## Slide 43: Specifying composition axes
Zr2O2a[Va]2(1-a)
Zr2O2(1-a)[Va]2a
NOTE: prim.json determines formula unit (2 Zr)

## Slide 44: Data Management
Project data is managed according to the parameters, settings, and timeline that it depends on:
  ‘calctype’ DFT parameters and setting (XC functional, pseudopotential, convergence parameters, etc.)
  ‘property’ The particular quantity being measured (formation_energy, volume_relaxation, etc.)
  ‘ref’ Baseline reference used for measuring quantity (zero-point of energy, reference volume, etc.)
  ‘bset’ Basis functions used to “fingerprint” configurations and in terms of which the property model is expressed .
  ‘eci’ The model parameters (effective cluster interactions) used to predict a particular property in terms of a particular basis set.
Manage and create settings profiles from the ‘casm settings’ command. A ‘default’ profile is created during project initialized.
Ex:
  DFT-calculated properties: Depend on ‘calctype’, ‘property’, and sometimes ‘ref’
  Cluster expansion/physics model: Depends on ‘calctype’, ‘property’, ‘ref’, ‘bset’
  Predicted properties and Monte Carlo Data: Depend on ‘calctype’, ‘property’, ‘ref’, ‘bset’, and ‘eci’

## Slide 45: Data Management Workflow
Info/Analysis
Configuration Database
Records configurations that have been enumerated or imported to a project and their associated data
Configuration Selection
References to subset of the configuration database.
CASM
Configuration Selection
Job Dispatch

## Slide 46: Working with selections
CASM query syntax provides simple interface to explore, screen, and select configurations.
Example:
casm select --set "eq(scel_size, 4)"
will select all configurations the belong to supercells of volume 4 (relative to primitive cell)
Many configuration properties are supported
  ‘scel_size’ Integer volume of supercell that contains the configuration
  ‘comp(a)’, ‘comp(b)’, etc. The chemical composition, in terms of composition axes
  ‘atom_frac(Au)’, etc. The atomic fraction of a particular specie
  ‘is_calculated’ True if DFT data exists for the configuration
  ‘formation_energy’ DFT formation energy (if calculated)
  ‘volume relaxation Change in volume due to relaxation (expressed as V/V0)
… and many others (for full listing see casm select --help properties)
Properties can be related and compared via operators
  arithmetic add, subtract, multiply, divide, sqrt, exp
  comparison equality, less-than, greater-than, etc.
  logical AND, OR, NOT, etc.
  ranges min, max, and others
  text search and match with regular expressions
for documentation see casm select --help operators

## Slide 47: Working with selections
Selections can be edited and combined using ‘casm select’
The ‘MASTER’ selection is stored in the configuration database and is the default selection for most operations. A selection can be redirected to a file using --output <filename>
Selection(s) to be operated can be read from a file using --configs <filename>
Edit selections using CASM query syntax
casm select --set <query> Create a selection from scratch
casm select --set-on <query> Set ‘selected’ from false to true if <query> is true
casm select --set-off <query> Set ‘selected’ from true to false if <query> is true
Combine selections using logical operators (AND, OR, NOT, XOR)

## Slide 48: Working with selections
Selections can be edited and combined using ‘casm select’
The ‘MASTER’ selection is stored in the configuration database and is the default selection for most operations. A selection can be redirected to a file using --output <filename>
Selection(s) to be operated can be read from a file using --configs <filename>
Edit selections using CASM query syntax
casm select --set <query> Create a selection from scratch
casm select --set-on <query> Set ‘selected’ from false to true if <query> is true
casm select --set-off <query> Set ‘selected’ from true to false if <query> is true
Combine selections using logical operators (AND, OR, NOT, XOR)
Predefined selections:
‘ALL’: specifies the total configuration database.
‘CALCULATED’: specifies all configurations for which DFT data exist.
‘NONE’: equivalent to ‘ALL’ but with all ‘selected’ bits set to 0

## Slide 49: CASM Query Syntax, Part II
CASM query syntax provides simple interface to explore, screen, and select configurations.
Use ‘casm query’ to print properties of selected configurations (supports JSON and CSV)
Example:
casm query --columns "comp(a)" "formation_energy" --configs select.csv
will print ‘casm select’-style CSV output to the screen:
output can be redirected to a file with --output <filename>
Query syntax can also be used to screen configurations at the enumeration stage, so they don’t pollute the configuration database.
Example:
casm enum --configurations --all --filter "lt(atom_frac(O),0.25)"
will only enumerate configurations that are dilute in oxygen (having O atomic fraction less than 0.25)

## Slide 50: DFT calculations
Provide DFT code input files and parameters
  Pseudopotentials, k-point density, energy cut-off, and settings files
Use ‘casm select’ to identify a selection of configurations to calculate
casm-calc --submit --configs my_selection.csv
  vasp.relax is python script that automates job submission for each configuration. It submits the DFT calculation, handles common errors, ensures that results are converged and relaxed, and writes results to a format CASM understands (properties.calc.json).
  Uses ‘pbs’ python module to automate job submission (https://github.com/prisms-center/pbs)
Current support for VASP and SeqQeust; QuantumEspresso partially completed, and support for other codes is planned. Contributions from the user community are encouraged!

## Slide 51: properties.calc.json files
CASM interprets calculation data from properties.calc.json file
Generated by ‘vasp.relax’ or manually using ‘vasp.relax.report’
$ROOT/training_data/$SCEL/$CONFIGID/calctype.$CALCTYPE/

## Slide 52: Relaxations and Mapping/Import
casm update:
  Read all new property files, and check relaxation
lattice_deformation (LD):
  Degree of homogeneous strain (per atom)
basis_deformation (BD):
  Mean square displacement
total deformation cost:
  w*LD+(1-w)*BD , 0<w<1
casm import:
  Use same algorithms as casm update to add ideal or relaxed configurations to project (even if not enumerated)
Very large relaxations may change the configuration. Conflicts can be resolved using either min-energy or min-deformation rule

## Slide 53: Setting energy reference
Chemical energy can only be measured relative to reference compounds

## Slide 54: Setting energy reference
Chemical energy can only be measured relative to reference compounds

## Slide 55: Setting energy reference
Chemical energy can only be measured relative to reference compounds
casm ref --set-auto will attempt to set energy references as near to extreme stoichiometries as possible (left case)

## Slide 56: CASM: Clusters Approach to Statistical Mechanics
First-principles energies of a “few” excitations
Lattice Model Hamiltonian
Monte Carlo
Thermodynamics
Extrapolate to
all other excitations

## Slide 57: Zr-O system
Puchala and Van der Ven, Phys. Rev. B 88 094108 (2013).
Each red circle specifies belongs to a specific configuration of HCP-based ZrOx

## Slide 58: Zr-O system
ZrO1/3
ZrO1/2
ZrO1/6
Puchala and Van der Ven, Phys. Rev. B 88 094108 (2013).
A
BC
A
BC
A
BC
A
-
B
C
A
-
-
A
B
C
A
B
C

## Slide 59: Zr-O system
O stacking sequences
Puchala and Van der Ven, Phys. Rev. B 88 094108 (2013).
ZrO1/6-ZrO1/3
ZrO1/3-ZrO1/2
ZrO1/6 if X = 0
ZrO1/2 if X = 2/3
de Fontaine, Nature 343, 544 (1990).

## Slide 60: CASM: Clusters Approach to Statistical Mechanics
First-principles energies of a “few” excitations
Lattice Model Hamiltonian
Monte Carlo
Thermodynamics
Extrapolate to
all other excitations

## Slide 61: The Clusters Approach to Statistical Mechanics
Is there a compact way to approximate the energy of any configuration?
x
y

## Slide 62: The Clusters Approach to Statistical Mechanics
Species A
Species B
Is there a compact way to approximate the energy of any configuration?
x
y

## Slide 63: The Clusters Approach to Statistical Mechanics
Is there a compact way to approximate the energy of any configuration?
Species A
Species B
x
y

## Slide 64: The Clusters Approach to Statistical Mechanics
Is there a compact way to approximate the energy of any configuration?
Species A
Species B
x
y

## Slide 65: The Clusters Approach to Statistical Mechanics
Is there a compact way to approximate the energy of any configuration?
Species A
Species B
x
y

## Slide 66: The Clusters Approach to Statistical Mechanics
Is there a compact way to approximate the energy of any configuration?
Species A
Species B
x
y

## Slide 67: The Clusters Approach to Statistical Mechanics
Is there a compact way to approximate the energy of any configuration?
Species A
Species B
x
y

## Slide 68: The Clusters Approach to Statistical Mechanics
Species A
Species B
x
y
The orbit of the the NN pair
Is there a compact way to approximate the energy of any configuration?
Symmetric averages of measurements of cluster occupation states.

## Slide 69: The Clusters Approach to Statistical Mechanics
Species A
Species B
x
y
Is there a compact way to approximate the energy of any configuration?
Symmetric averages of measurements of cluster occupation states.

## Slide 70: The Clusters Approach to Statistical Mechanics
Is there a compact way to approximate the energy of any configuration?
Symmetric averages of measurements of cluster occupation states.
Species A
Species B
x
y

## Slide 71: The Cluster Expansion
Species A
Species B
x
y

## Slide 72: The Cluster Expansion
The occupant of lattice site i is described by the variable σi :
σi = +1 if species A
σi = -1 if species B
σ15
σ16
σ17
σ14
σ5
σ6
σ18
σ13
σ4
σ1
σ7
σ19
σ12
σ3
σ2
σ11
σ10
σ9
σ8
Species A
Species B

## Slide 73: The Cluster Expansion
Interactions between sites are described by products of σi .
Fit interaction parameters to a database of DFT energies.
Then use symmetry to average over the entire crystal
E = J11 + J1,717 + J1,18118 + J1,17117 + J1,4,5145 + . . .
σ15
σ16
σ17
σ14
σ5
σ6
σ18
σ13
σ4
σ1
σ7
σ19
σ12
σ3
σ2
σ11
σ10
σ9
σ8

## Slide 74: Cluster Expansion Example
σ15
σ16
σ17
σ14
σ5
σ6
σ18
σ13
σ4
σ1
σ7
σ19
σ12
σ3
σ2
σ11
σ10
σ9
σ8

## Slide 75: Cluster Expansion Example
σ15
σ16
σ17
σ14
σ5
σ6
σ18
σ13
σ4
σ1
σ7
σ19
σ12
σ3
σ2
σ11
σ10
σ9
σ8
Average site occupation is Γ1=(1 + 6)/2=0

## Slide 76: Cluster Expansion Example
σ15
σ16
σ17
σ14
σ5
σ6
σ18
σ13
σ4
σ1
σ7
σ19
σ12
σ3
σ2
σ11
σ10
σ9
σ8
Average site occupation is Γ1=(1 + 6)/2=0

## Slide 77: Cluster Expansion Example
σ15
σ16
σ17
σ14
σ5
σ6
σ18
σ13
σ4
σ1
σ7
σ19
σ12
σ3
σ2
σ11
σ10
σ9
σ8
Average site occupation is Γ1=(1 + 6)/2=0
Average NN pair occupation is Γ2=(17 + 16 + 15 + 618 + 617 + 616)/6 = 1/3

## Slide 78: Cluster Expansion Example
σ15
σ16
σ17
σ14
σ5
σ6
σ18
σ13
σ4
σ1
σ7
σ19
σ12
σ3
σ2
σ11
σ10
σ9
σ8
σ15
σ16
σ17
σ14
σ5
σ6
σ18
σ13
σ4
σ1
σ7
σ19
σ12
σ3
σ2
σ11
σ10
σ9
σ8
Correlations are identical for symmetrically equivalent configurations

## Slide 79: The bspecs.json file
Specifications for generating clusters and the cluster expansion basis functions

## Slide 80: The clust.json file
Lists one example (“prototype”) of each cluster type

## Slide 81: The clexulator (ZrO_Clexulator.cc)
Generated code for evaluating basis functions
Generated code for evaluating basis functions

## Slide 82: Cluster expansion for hcp Zr-O

## Slide 83: Cluster expansion for hcp Zr-O
Puchala and Van der Ven, Phys. Rev. B 88 094108 (2013).

## Slide 84: CASM: Clusters Approach to Statistical Mechanics
First-principles energies of a “few” excitations
Lattice Model Hamiltonian
Monte Carlo
Thermodynamics
Extrapolate to
all other excitations

## Slide 85: Summary
Crystal structure identification & specification
Symmetry analysis
Using CASM to manage data
  Configuration selections and query syntax
  Maintaining sanity with cluster expansion profiles
Cluster expansion basics
  Configuration enumeration
  Cluster expansion basis sets & correlation evaluation
After break:
Parameterizing cluster expansions
Predicting thermodynamic properties with grand canonical Monte Carlo
Free energy integration and phase diagram construction